## Slide 1: Seizure Detection using EEG
Akhil Jain – 2011CS50274
Mayank Gupta – 2011CS50283
Notes: Hi
This presentation is for the project done as a part of the course EEL781 – Neural Networks. This project is on detection of seizures using EEG and has been done by Akhil Jain and Mayank Gupta.

## Slide 2: Motivation
Prevalence of seizures in neo natal babies
10% detection rate
Challenge of multi-channel inputs
Need for a real-time seizure detector for clinical use
Notes: First let’s talk about what is the need for this project. Temko tells us about a significant number of cases where neonatal babies have been affected by seizures and how traditionally, these seizures are manually detected by studying the EEG of a baby in an ICU. However, it has been estimated that only about 10% of the seizures are clinically detected due to various reasons like the absence of trained experts round the clock, difficulty in keeping track of multiple input channels and human error. In such a scenario, it is paramount that an automatic seizure detection system be developed so as to enable trained medical professionals to take quick and necessary action. Also, any system so developed must be fast enough to be able to give real time estimates on the nature of an input data segment.

## Slide 3: Dataset
Provided by the UPenn - Mayo Clinic Seizure Detection Challenge on kaggle.com, sponsored by the American Epilepsy Society, and the data is available via the NIH-sponsored International Epilepsy Electrophysiology Portal (ieeg.org)
Notes: For this study, the data has been taken from the Kaggle Seizure Detection Challenge website and corresponds to 8 patients as described in the adjoining table. Each patient has a different number of channels associated with his segments. However, it is the same across all segments of that patient.

## Slide 4: Method
Use of an SVM based classifier
Use of mean across channels – focus on speed at the cost of accuracy
RBF Kernel with 21 features drawn across different domains
Notes: A survey of multiple modelling techniques was done by Garrett et al and it was concluded that an SVM is the most powerful machine for the purpose. Therefore, in this study, we use an SVM to classify incoming segments into interictal or ictal. Since we are willing to sacrifice correctness at some times for much greater speed, we would be using the mean of features calculated over all channels as the representative of a data segment. We then use a RBF kernel on these data points to train, validate and test. The features have been picked across domains and have been proven to be the best features by Greene et al in their work.

## Slide 5: Time domain features
Line length
RMS Amplitude
Zero crossings
Minima and Maxima
Nonlinear energy
Hijorth Parameters
  Activity
  Mobility
  Complexity
AR Model Fit
Notes: The time domain features are as shown on this slide. It is generally expected that there is a marked change in complexity when a seizure occurs. And in keeping with this notion, the various features that can determine the order of complexity of the curve are taken into consideration while computing the time domain features. It is to be noted that most of these features have already traditionally been used in epileptic seizure detection in adults and the present application is just an extension of the same. The time domain features are the most important ones. In fact, it has been shown that the accuracy of a classifier based only on time domain features is comparable (although less) to that of one based on multiple domain features.

## Slide 6: Frequency Domain Features
Bandwidth
Peak Frequency
Peak Power
Spectral Edge Frequency
Total Spectral Power
Intensity Weighted Mean Frequency
Intensity Weighted Bandwidth
Wavelet Energy
Notes: The frequency domain provides another view of the EEG signal and can be used to outline the variations that take place with the onset of a seizure. In this domain, the wavelet energy is the most important one. Many a times, it has been used by itself (along with a genetic algorithm) to detect seizures in EEG signals. All other features are basically a measure of the power carried by the signal and significant variations in the same are expected in the event of a seizure.

## Slide 7: Entropy Domain Features
Spectral Entropy
Shannon Entropy
Approximate Entropy
SVD Entropy
Notes: It is expected that the onset of a seizure would reduce the complexity of the brain, thereby impacting entropy. Therefore, four similar measures are used to classify data segments. Although they may appear to be similar at first glance, it is to be noted that the slight variations in each form of entropy is significant enough to gain a better classifier over the dataset.

## Slide 8: Testing Paradigm
Patient wise iterative testing and validation on mean normalised feature sets
Precision and Recall – better measures of measuring the fitness of a model
Simulation of real life situations
Notes: In our testing paradigm, we iteratively moved through the patients, training on 6, validating and tuning on the 7th and then testing on the 8th. Accuracy of prediction does not provide a good enough measure of the robustness of the algorithm since the number of interictal segments is much higher than the ictal and we would gain an appreciable amount of accuracy by just predicting all to be interictal. Therefore, we use measures like precision and recall to be able to make a better estimate of the health of our classifier. Also, it is to be noted that by opting for a patient-wise model instead of a truly random sample of training and validating sets, we are mimicking the real life situation wherein the data samples for only one given patient shall be available at any given point in time.

## Slide 9: Results
Mean Precision – 0.7236
Mean Recall – 0.6959
Mean F-measure – 0.7031
Mean Accuracy – 70.3785%
Notes: This table shows the results that were obtained during the tests as described previously. It is to be noted that the precision and recall values are almost comparable to the accuracy values for most cases. This demonstrates the fact that the SVM based classification algorithm is truly robust. Although the results are slightly discouraging in that the literature reports accuracies over 90%, it is to be noted that the detection is fast in this case – something that hasn’t been achieved for most classifiers until now. Therefore, this tradeoff between speed and accuracy is justified.

## Slide 10: Conclusions
Significant time gains
Accuracy much higher than the traditional manual detection of seizures
Exploration of the method with more ictal data points is something that can be explored in future work
Notes: In conclusion, we can say that the project was able to give us a classifier that’s much faster than previously done work and provides a much higher accuracy than the traditionally used manual detection through visual inspection of the EEG. One of the possible reasons for the low accuracy might be that the number of ictal points as compared to the interictal points is very low and therefore the SVM may lead to some sort of overfitting on the training dataset. We need a lot many more training points to be able to accurately compute the effectiveness of this approach. Until then approximately 70% accuracy that is achieved in the current approach is an achievement in itself.